Testing the control software
Bill Mania
bill@manialabs.us
26 Oct 2018
v2

Environments and their properties for testing the control software on the Riptide μUUV. There will be three main objectives during testing:

1. Generate meaningful results from the testing
2. Minimize damage to the vehicle
3. Prevent loss of the vehicle

This document acknowledges lack of connectivity with the vehicle while testing beneath the surface and inconsistent connectivity with the vehicle while it is on the surface. It initially expects crude dead reckoning navigation from the current Riptide implementation. It’s assumed there will be consistent, high quality connectivity with at least one of the main vehicle computer (BeagleBoneBlack) and the control computer (Raspberry PI) during benchtop testing.
What this document does not address is how to perform large area and long duration testing of locating and tracking a plume of Rhodamine WT dye. The dye is very expensive to acquire. It will be expensive to deploy a plume source in a way which simulates the expected contest environment. There may be regulatory constraints on releasing a plume in the Bay, too.

### Benchtop
1. Electrical power
  1. voltage steady
  2. unlimited duration
2. Navigation data
  1. no GPS
  2. fixed pose
3. Dye sensor
  1. will use simulated dye data
4. Vehicle damage and loss
  1. minimal risk of damage
  2. no risk of loss
  3. drop weight easily tested
5. Duration of operation
  1. computers, control surfaces, dye sensor unlimited
  2. propulsion motor very limited
6. Communication
  1. high quality
### Swimming pool
1. Electrical power
  1. batteries
2. Navigation data
  1. good GPS on the surface
  2. Riptide dead reckoning beneath
  3. Highly chlorinated freshwater – may affect dead reckoning and buoyancy
3. Dye sensor
  1. unlikely to add dye to the pool
  2. calibration may be affected by water density and chlorine
4. Vehicle damage and loss
  1. damage likely due to small volume with hard walls
  2. no risk of loss
  3. drop weight easily tested
5. Duration of operation
  1. all systems operable until batteries exhausted
  2. time in the pool is limited
6. Communication
  1. consistent from the surface
### Shallow area of the Bay
1. Electrical power
  1. batteries
2. Navigation data
  1. good GPS on the surface
  2. Riptide dead reckoning beneath
3. Dye sensor
  1. can add some dye to the Bay, but probably not an adequate quantity
  2. calibration good
4. Vehicle damage and loss
  1. damage more likely due to submerged obstacles
  2. risk of loss low
  3. drop weight will likely be lost
5. Duration of operation
  1. battery life
6. Communication
  1. consistent within range from the surface
### Deep area of the Bay
1. Electrical power
  1. batteries
2. Navigation data
  1. good GPS on the surface
  2. Riptide dead reckoning beneath
3. Dye sensor
  1. can add some dye to the Bay, but not an adequate quantity
  2. calibration good
4. Vehicle damage and loss
  1. damage less likely due to lower ratio of obstacles but greater chance of collision with traffic
  2. risk of loss high
  3. drop weight will be lost
5. Duration of operation
  1. battery life
6. Communication
  1. consistent within range and line-of-sight from the surface
### Offshore
1. Electrical power
  1. batteries
2. Navigation data
  1. good GPS on the surface
  2. Riptide dead reckoning beneath
  3. most affected by currents
3. Dye sensor
  1. can add dye, but not an adequate quantity
  2. calibration most realistic
4. Vehicle damage and loss
  1. damage least likely due to lower ratio of obstacles and low chance of collision with traffic
  2. risk of loss high
  3. drop weight will be lost
5. Duration of operation
  1. battery life
6. Communication
  1. consistent within range from the surface
### First control test
The first test is designed to verify the software can control the speed and direction of the AUV. It will acquire a 2D position, waggle the control surfaces, then dive to N meters. It will then climb to the surface and stop the propeller. When the instruments indicate the AUV is on the surface, it will waggle only a single control surface.
This test will be conducted on the bench first (simulating depth and position data) and then conducted in the pool.