NOAA bonus prize design
Bill Mania <bill@manialabs.us>
26 Oct 2018

### Use Cases

- Update GPS position periodically
  To compensate for drift in the odometry map and reduced accuracy from IMU dead reckoning, periodically return to the surface long enough to
  - acquire 3D GPS fix
  - acquire heading
  - dump logs and look for ABORT command
- Stay within geographic boundaries of the volume
  The search volume will have four horizontal boundaries and two vertical boundaries. The two vertical will be the surface and the maximum depth. Frequently compare the vehicle position to the interior of the volume. When the vehicle is near a boundary, adjust the heading to keep the vehicle within the volume.
  - Is the vehicle within the volume
  - What’s the range and bearing to the nearest boundary and to the center of the volume
- Measure the local level of the dye and update the map
  Using the dye sensor, establish a local level of the dye. Adjust that measurement for the current gain level, retrieve the current vehicle position, determine the cell in the map, combine the previous measurement for that cell with the current measurement, and update the cell.
- Look for a plume in the map and update the search plan
  The dye is expected to disperse more through a curved cone and less through an expanding sphere. As measurements are collected in the map, look for lines going from lower levels to higher levels and weight the vehicle’s search direction along the line toward the higher levels.
- Calibrate the dye sensor
  With the vehicle in or very near to the volume, establish a background measurement for the dye.
- Surface when battery level drops below threshold
- Surface when time limit expires
- Surface when failure occurs
- Search the volume of seawater, navigating and updating dead reckoning position
- Update the search plan based on time elapsed
  As time elapses, the dye will become more and more dispersed. Use that information to inform the way measurements update the map.
- Set volume boundaries
  Once before the actual search starts, record the definition of the search volume as provided by the contest organizers.
- Adjust dye sensor gain
  As the vehicle navigates closer to the source of the dye and the measurements of the dye increase in strength, adjust the gain so as not to overwhelm the measurement calculations.
- Set the starting pose
  Using a pose determined by high-accuracy instruments, set the vehicle’s current pose.
- Initialize parameters which will be used with dye dispersal and navigation calculations

### Considerations

1. The dispersal characteristics of the dye, incorporating time, temperature, and current.
  1. Search online for details for “rhodamine WT”
2. The integration of Cyclops sensor with the vehicle
  1. Depending on Riptide to integrate it. Will be in the nose. Talk to Dean.
3. The integration of the Raspberry Pi with the vehicle
  1. Add a Raspberry Pi and connect via Ethernet. Provide OS image to Stephen. BeagleBoneBlack.
4. Verification of the complete Riptide MOOS solution
  1. GPS and IMU integration to provide pose information
  2. Calibrate the accuracy of the vehicle’s dead reckoning position
  3. Talk to Dean
5. Reconcile the contest maximum depth with the vehicle’s capability
  1. software limit the device to 200m depth, contest may not go that deep.
6. Competitors
  1. John Hurtado at Texas A&M? hurtado@aero.tamu.edu – no idea
  2. Stephen will talk to folks from MBARI about tracking plumes
7. Testing of the vehicle
  1. On the bench
  2. In the pool – can get remote WiFi access with long cable
  3. In the Bay
    1. parts of Raccoon Strait are 50 meters
    2. large General Anchorage 5 is 11 meters
    3. Golden Gate is 91 meters (but very busy and lots of obstacles
  4. Morro Bay, Monterey Bay
  5. Any regulations on the operation of UUVs or AUVs?
8. Fail safe
9. Second Riptide UUV coming
10. Contest scheduled for end of Jan 2019 near Puerto Rico

### Objects
1. Auv
   The Riptide μUUV, its sensors, and actuators.
  1. Attributes
    1. current pose
    2. dye sensor reading
    3. control surface and propeller settings
    4. battery level and watchdog timer
  2. Actions
    1. set the trajectory based on the search path
    2. update the pose with navigation data
    3. update the pose with GPS data
    4. release the ballast
2. SearchSpace
   The 3D map of the volume of seawater in which the Auv operates.
  1. Attributes
    1. knowledge of each visited cube in the space
    2. estimate of the location of the plume source
    3. current search path
    4. currents in the water
  2. Actions
    1. update the information about a cube in the space, converting the auv’s geo coordinates to a specific cube
    2. update the plume source estimate, using the locations of each cube where dye was detected
    3. define the boundaries
    4. calculate a bearing and range to the plume source estimate
    5. calculate a bearing and range to the plume
    6. calculate an updated search path
    7. determine if the auv has left or is about to leave the search space