Dye sensor requirements
Bill Mania
bill@manialabs.us
25 Oct 2018
v1

A description of the requirements for integrating a Turner Cyclops 7F Rhodamine WT sensor with a Riptide μUUV and MOOS.

1. The sensor is located at the front of the vehicle, to maximize its exposure to the seawater environment as the vehicle moves
2. The gain of the sensor must be adjustable via software at run-time
3. The sensor reading must be published at a rate of one Hertz
4. The current sensor reading is published via the MOOS variable DYE_VALUE
  1. Positive floating point value
  2. Inclusive range of 0.00 to 5.00
  3. 0.00 indicates seawater with no detectable dye
  4. 5.00 indicates pure dye with no seawater
  5. Rounded to the nearest 0.01
5. The current gain setting must be published at a rate of one-tenth Hertz
6. The gain of the sensor is adjusted using the MOOS variable DYE_SET_GAIN
  1. Positive integer value
  2. One of 1, 10, and 100
7. The current gain setting is published via the MOOS variable DYE_GAIN
  1. Positive integer value
  2. During normal operation, one of 1, 10, and 100
  3. A special gain value of 0 indicates an error with the sensor system
8. The sensor can be placed in CALIBRATION or OPERATION mode
9. The mode of the sensor is set by the MOOS variable DYE_MODE
  1. String value
  2. A value of “CAL” will reset the sensor system, halt the publishing of DYE_VALUE, set the DYE_GAIN value to 1, and begin sampling the current environment, treating it as the background for a DYE_VALUE of 0.00
  3. A value of “OP” will complete the calibration process and place the sensor in OPERATION mode
10. A defined latency between reading the sensor value and publishing the MOOS variable
  1. Latency no greater than 100 milliseconds
  2. Variation in latency no greater than 10 milliseconds