Network connectivity
Bill Mania
bill@manialabs.us
25 Oct 2018
v1

The requirements for optimal network connectivity with the Riptide μUUV, for both the main vehicle computer (BeagleBoneBlack) and the control computer (Raspberry Pi 3). The requirements cover two scenarios, the Riptide on the bench and in the water.

### Control computer
The control computer has two network interfaces onboard: wireless and wired.
The wired interface will have a fixed IP address and will be connected directly to the wired interface of the main vehicle computer. It will be used for communication between the control software running on the control computer and the MOOS software running on the main vehicle computer.
When the vehicle is on the bench the wireless interface will have outbound connectivity with the public Internet and two-way connectivity with the project notebook computer. The Internet path will be used for software updates and installations. The path with the notebook computer will be used for administrative access to the control computer.
When the vehicle is in the water the wireless interface will connect (and reconnect) with the project’s Access Point, whenever possible. This path will be used for administrative access with the control computer during testin and competition.
### Main vehicle computer
The main vehicle computer also has two network interfaces: wireless and wired.
The wired interface will have a fixed IP address, on the same network as the control computer’s wired interface, and will be connected directly to the control computer’s wired interface. The interface will be used for communication between the MOOS software running on the main vehicle computer and the control software running on the control computer. The wired interface will also be used as a path for administrative access to the main vehicle computer, via the control computer.
When the vehicle is on the bench its wireless interface will have outbound connectivity with the public Internet. This path will be used for software updates and installations.
When the vehicle is in the water the wireless interface will not be used, in order to avoid conflict with the control computer’s wireless interface and to reduce electrical power consumption.
### Optional connectivity
As a safeguard and for out-of-band connectivity, the serial console of the main vehicle computer can be connected to the USB of the control computer. This will provide an alternate path for administrative access to the main vehicle computer.